X Server Configuration
Configuration file :
    - /etc/X11/XF86Config or /etc/X11/xorg.conf
The video card , monitor, keyboard and mouse configuration is stored in this file.
The file has specifies the hardware components in the following sections
  - Server Layout : Defining individual combination of 'Input Devices' and 'Screen' .
  - Module : Defining which hardware and extension specific module are called when X is started.
  - Input Devices : Defining keyboard , mouse , touchscreen , or other form of supported input devices.
  - Monitor : Defining Characteristics and capabilities of the physically attached output hardware.
  - Device : Defining which hardware specific driver is used to communicate with the local video card.
  - Screen : Defining individual combination of “Monitor” and “Devices” with display properties.
X server has a lot of dynamically loadable Loadable Modules :
  - Drivers : ati , s3virge , neomagic , fbdev , etc .
  - Extensions : glx , dri, etc .
In Redhat Enterprise Linux the server component are stored in the file :
  - /usr/X11R6/bin/XFree86

---
X Font Server Configuration
xfs is the Xfree86 font Server.
  - In RHEL 4.0 configuration file is stored in the location /etc/X11/fs/config .
  - X-enabled Linux system run their own font server.
Font server can be network enabled :
  - Individual workstation need not archive large amount of fonts locally.
  - Centralized font management.
  - Default xfs configuration allows only localhost .
Adding font directories to the xfs
  - Chkfontpath
  - Edit /etc/X11/fs/config
  - Add fonts to the ~/.fonts and run the command fc-cache as root.

---
Questions ???